## Slide 1: Flexible PCB’s Design and Stack-Ups
Presented by Royal Flex Circuits and Insulectro
Royal Flex Circuits: Bob Meyer – Larry Ybarra
And Insulectro: Chris Hunrath

## Slide 2: Royal Flex Circuits
Quick Turn PCB Flex & Rigid-Flex Specialist:
Over the last 30 years, Royal Flex Circuits has become the leader in quick-turn, high-tech PCB manufacturing – with no minimum order quantity. Using the latest technology and cutting-edge equipment, we are building the Factory of the Future with the capability to manufacture from the most basic to todays industry leading technology.

## Slide 3: Royal Circuits Group
Rigid
Hollister, CA
Quick turn, turn key, FR4, Polyimide, HSD and RF. Heavy copper (> 3.0 oz). Proto to production.
Flex, Rigid-Flex, Rigid and Assembly
Santa Fe Springs, CA
Quick turn, specialty applications
Royal Flex Circuits, in Santa Fe Springs, CA. is part ot the Royal Circuits Group, a highly recognized PCB company with manufacturing facilities in both Northern and Southern California. Royal Flex Circuits moved into a new, custom build production facility a little over a year ago, featuring the latest machinery, hardware and production methods.

## Slide 4: Insulectro: Electronic Materials
Offer a wide range of PCB materials from premier suppliers.
  Isola, DuPont, LCOA, CAC, Pacothane, Oak Mitsui, JX Nippon
Maintain the critical mass required to provide better access to products and technical support for the electronics industry.
  Provide Local Inventory
    Customers access material in hours
  On-site technical support
ACT! Accomplish Change Together
  Support fabricators with their customers
  Provide support for proper material selection

## Slide 5: Materials for many technology Applications

## Slide 6: Why Flex?

## Slide 7
Bend to Install

## Slide 8: Design Success
PCB’s are no longer simple replacements for wires.
They are an integral part of the design.
You don’t need to be material science experts.
Many of the new materials bring technology and/or performance advantages.
We are here to help.

## Slide 9: Overview: Design Considerations
Bend to install or occasional flex or dynamic flex (and everything in between).
  Bend directions, bend axis
  Bend radius
Electrical
  Speed, frequency, bit rate, high current, high voltage
RF, noise, EM environment.
Operating temperature.
Use environment.
  Indoor, outdoor, medical, outer space, under hood

## Slide 10: General Flex PCB Types

## Slide 11: Cost Drivers: Stiffener vs Rigid Flex

## Slide 12: Flex Materials

## Slide 13: Flex IPC Spec’s
Fab
  IPC-6013 (IPC-6012 for rigid)
Materials
  IPC-4202 – Base films
  IPC-4203 - Adhesive systems (Sheet adhesive, Coverlay, Bondply)
  IPC-4204 – Metal Clad dielectrics
  IPC-4562 – Metal Foils

## Slide 14: Overview: Film Types
Type | Properties | Applications
Pyralux AP, AG and AC | Copper clad All Polyimide Film | Basic clad building block for circuits
LF and FR Adhesive | Acrylic Thermoset | Coverlay, bondply Multilayer
Pyralux GPL Adhesive (New) | Thermoset Epoxy Blend | Coverlay, bondply multilayer
Pyralux HT | Thermoplastic Polyimide | Coverlay, bondply High Temp, High Speed
Pyralux TK | Teflon/Kapton composite | Coverlay, bondply and clad Very High Speed

## Slide 15: Bulk Properties of FPC Dielectric Films
Property | Unit | Method | Kapton® HN | Pyralux® AP | Pyralux® HT Bondfilm | Pyralux® TK | LCP
Thicknesses | mil | – | 1 - 5 | 1 - 6 | 1-4 | 2 – 4 | 1, 2, 4
Dk @ 10 GHz | – | Method 2.5.5.5 | 3.4 | 3.2 | 3.0 | 2.5 | 3.0 - 3.1
Df @ 10 GHz | – | Method 2.5.5.5 | 0.010 | 0.002 - 0.003 | 0.003 | 0.002 | 0.001 - 0.002
% Moisture uptake | % | Method 2.6.2 | 2.8 | 0.8 | 0.8 | 0.6 | 0.04
CTE (x-y axis) | ppm/°C | 50 to 250 °C | 20 | 25 | 25 | 27 | 18
CTE (z axis) | ppm/°C | 50 to 250 °C | 115 | 90 | 90 | 102 | 120
Peel strength | N/mm | IPC-TM650 | N/A | 2.0 (ED) 1.6 (RA) | N/A | 1.2 (RA) | 1.0 (ED) 0.4 (RA)
Tg | °C | DMA | 360 - 410 | 220 | 220 | 270 | –
Tm | °C | DSC | – | – | – | 300 | 280 - 315
Flammability | – | UL94 | V-0 | V-0 | V-0 | V-0 | V-0
Notes: Consolidated Industrial product roadmap

## Slide 16
Combination of the following;
  Material loss (Df)
  Conductor (Copper Trace)
    Trace roughness
    Trace width and thickness
    Trace Length
Total loss = Dielectric loss + Conductor Loss
Signal integrity is often the most important need in a design.
As speed increases, loss becomes more important.
Rolled Annealed Copper performs well at high speeds

## Slide 17: Dk and Df of Pyralux Materials
Kapton® (The heart of AP and AG) Dk and Df depends on…
  Type
    Type used in FR and LF Coverlay/Bondply is more lossy than that used in AP
  Orientation (normal or in-plane)
    Dk in-plane is higher than Dk normal
    Df about the same in both directions
  Environment (moisture level)
    Generally loss will increase significantly in humid environments if not encapsulated by copper.
    Dk will increase very slightly due to humidity (not significantly)
Dk = 3.1 – 3.6
Df = 0.004-0.012
Dk = 2.9-3.5
Df = 0.02-0.03
Acrylic Adhesive
  Huge frequency dependence for Dk (3.5 at MHz, 2.9 at GHz).
  Loss about 10 times more than Kapton® and 100 times more than Teflon®.
  High frequency applications should minimize the amount of acrylic in the stack-up.
Normal Dk is used in analysis

## Slide 18: Microstrip Basics
Structure
  Two metal layers – ground and signal
    Usually a coverlay laminated to top and bottom (not shown here)
    Coverlay is a “necessary evil” to protect the copper. Slightly affects impedance and increases loss.
  Advantage: Lowest loss transmission possible with laminate materials.
  Disadvantage: Susceptible to outside noise
Fundamentals
  Signal is transmitted as WAVES of a changing electric field propagating through the dielectric
  More field lines pass through the clad than the coverlay.
  Impedance is determined by
    Dielectric constant
    Thickness of dielectric
    Width of line
    Thickness of copper
Structure Used
Copper Resistance
Roughness of copper
Loss tangent of dielectric
Loss is determined by
Electric Field Lines Shown
Ground
Signal
Clad
Coverlay
0
+

## Slide 19: More Details on Microstrip
Determining Line Width
  Coverlay shown in this example.
  Fabricators generally adjust to get the impedance they need by adjusting the line width.
  They use software to do design calculations to tell them what widths to assign given certain thickness and dielectric constant values.
  The results of this analysis are design curves like the one shown in the following slide.
Estimating Loss
  At low frequencies (<100 MHz), the main thing that determines signal loss is resistance of the copper.
  Fundamentally, thinner laminates will have higher loss. Recall the initial “pipe” example. Similar reasoning why narrow pipes are more lossy.
  At RF frequencies – the copper resistivity, dielectric loss and roughness are all contributors to loss.
  At high frequencies (>10 GHz), the roughness of the copper has the biggest effect on loss.
Bottom coverlay not electrically active
Hclad
W
T
Hcoverlay
Dkcoverlay
Dkclad
Ground
Signal

## Slide 20: Effect of Dielectric Constant

## Slide 21: Stripline Basics
Structure
  Three metal layers – ground-signal-ground
    Requires two laminations – one for bondply and the other for coverlay.
    More common in rigid-flex designs than microstrip.
  Advantage: Most noise-free structure since ground layers shield both top and bottom.
  Disadvantage: Thicker and higher loss than microstrip.
Things to Keep In Mind
  Stripline circuits need top and bottom ground planes to be tied together with vias.
  No electric field passes through the coverlay.
  Connectors are more difficult to implement with stripline, it may make more sense to use a rigid-flex approach to avoid use of connectors.
  Stripline has higher loss than microstrip due to the geometry and the fact that the line widths are normally narrower than microstrip.
Electric Field Lines Shown
Ground
Signal
Clad
Bondply
Ground
+
0
0

## Slide 22: Copper Effects
High Frequency Effects
  As frequency increases, the current concentrates more and more toward the edges of the volume of the copper.
  When the roughness of the copper surface becomes close to the wavelength of the signal, the loss increases.
  This begins to be a big factor at frequencies of 10 GHz and higher.
  The plot does not suggest that the dielectric loss decreases, rather it indicates that low profile RA performs better than predicted.
Rules of Thumb
  Thicker copper has slightly lower loss and wider lines have lower loss.
  Effects of oxide treatments are hard to accurately predict, but generally only have an effect at higher frequencies.
  Skin effect has a bigger impact on stripline than microstrip since field is concentrated on top and bottom of line instead of mostly the bottom.
copper
dielectric
Higher Loss at High Speed
copper
dielectric
Lower Loss at High Speed
Cu Trace Cross Sections (dark areas show highest field density)
Low frequency
High frequency

## Slide 23: Low Profile copper Reduces Signal loss
Smoother = lower loss
SEM’s of copper foil surfaces from standard to VLP2
High performance laminates are a balance between signal performance and thermomechanical performance.
Yes, these are at the same magnification.
Typically, HVLP or VLP2 coppers come at a cost premium

## Slide 24: Foil Grades from IPC 4562
Grade | Description
1 | Standard electrodeposited (STD-Type E)
2 | High ductility electrodeposited (HD-Type E)
3 | High temperature elongation electrodeposited (HTE Type E)
5 | As rolled-wrought (AR-Type W)
6 | Light cold rolled wrought (LCR type W)
7 | Annealed-wrought (ANN-Type W)
8 | As rolled-wrought low temperature annealable (LTA-Type W)
9 | Nickel, standard electrodeposited
10 | Electrodeposited low temperature annealable (LTA-Type E)
11 | Electrodeposited annealable (A-Type E)

## Slide 25: Thickness and Width
For Microstrip, the benefits of lower Dk are not as significant.
  Line widths are always wider for microstrip than stripline.
  Having a lower Dk coverlay would make the difference a little bigger, but not by much.
  The main motivation for a Teflon® based coverlay would be to improve the loss…it would make a big difference here.
Low Dk has the biggest impact on stripline designs.
  The impact of a 2 mil vs 3 mil line width is MUCH bigger than the impact of a 6 mil vs 7 mil line width.
  The lower Dk directly affect yields if thickness is fixed.
  Lower Dk enables thinner designs in other cases.
Cu 0.7 mil
Cu 0.7 mil
LF Coverlay 1 mil
LF Coverlay 1 mil
Clad 1-5 mil in plot
H
LF Coverlay 1 mil
Cu 0.7 mil
LF Coverlay 1 mil
Cu 0.7 mil
H
1 mil adhesive between clads. Total internal dielectric 3-7 mil in plot. Adhesive conforms to Cu

## Slide 26: Differential Pairs
What they are
  Two lines coupled together. They are either called “+” / “-” or “signal” / “return”.
  Example: Phone Lines – wires twisted together.
  Phone cable can be unshielded (like the one shown) or shielded with foil wire wrap.
Why use them?
  A changing current (aka “a signal”) will induce currents on nearby wires or traces.
  This is called “crosstalk” – probably have experienced it on telephone conversations.
  Coupling the signals together minimizes crosstalk due to the coupling (see electric field lines).
  Noise that is common to both “+” and “-” are much weaker than the coupling between the two signals.
  Stripline geometry provides the most immunity from external noise similar to the way shielded versus unshielded phone cable.
+
-
0
0
Differential Stripline
+
-
0
Differential Microstrip
UTP Cable

## Slide 27: Eye Pattern Testing on Covered MS Lines
REAL measurements. Not simulations (usually what you see).
FR4 – 4 mil Thick Pyralux® TK – 3 mil Thick 50 ohm, 200 mm Long 50 ohm, 200 mm Long

## Slide 28: Flexible Circuit Materials: General Guidelines
Use adhesive-less clads, AP and AG for most applications.
Use acrylic adhesive for most applications.
  Cost, Availability, Flexibility, ease of process
When not to use acrylic adhesive
  Low loss, high operating temperature
Use Rolled Annealed copper.
  Flexibility, Availability
For very thin (>9 micron) coppers, use ED foil

## Slide 29: Flexible Circuit Materials: Low Loss, High Speed
Polyimide films like Pyralux AP and AG outperform many rigid PCB materials – Df of 0.0030 and 0.0035 respectively
Acrylic adhesive is around 0.0250
The new GLP adhesive is 0.0035
The HT bondsheet is 0.0030
The TK bondply is 0.0020
Note: HT and TK require special lamination conditions at the fabricator.

## Slide 30
Rigid/Flex Stripline build with AP Clad and HT Film
Current Rigid/Flex Stripline with AP/LF “bikini” construction

## Slide 31: ROYAL FLEX CIRCUITS
Flex Building Blocks
Royal Flex Circuits EngineeringTeam will make recommendations for the best stack-up based on the design.
Design for fab, Design for success!

## Slide 32: Pyralux TK and GPL
GPL has great loss characteristics, and does not require high temperature lamination like HT does.
A combo of TK and GPL would yield a very low loss board without needing special processing requirements.
A low loss solution without needing investments
Products | DK | DF
Pyralux GPL | 2.8 | 0.0035
Pyralux TK | 2.5 | 0.002
* Would need to laminate GPL to Kapton, coverlay option of GPL coming later in 2020.

## Slide 33: HT Bonding Film – Used for Bondply or Coverlay
Homogeneous thermoplastic film.
  Similar to thermoplastic layer of AP or HT clad
  No curing or cross-linking involved
  Very viscous – no flow
Multi-Functional: Bondply or Coverlay
  No reinforcing film required due to high viscosity
  Different thicknesses available (1-4 mil)
Very good High Frequency Performance
  No Acrylic!
  Dk=3.2, Df=0.003
  Low moisture absorption

## Slide 34: Examples – HT as a Coverlay
HT9121R with HT0300
  - DS 1 oz Cu over 2 mil PI
  - 3 mil HT Coverlay
HT8525R with HT0200
  - DS 0.5 oz Cu over 2 mil PI
  - 2 mil HT Coverlay
HT9121R with HT0200
  - DS 1 oz Cu over 2 mil PI
  - 2 mil HT Coverlay
34

## Slide 35
Bend Ratio = Bend Radius : Thickness
10:1 Single Sided
10:1 Double Sided
20+:1 Multi-Layer

## Slide 37: Bend Area: General Guidelines
Keep single plane layer near center of stack-up.
Keep signal layers (traces) inside (concave side) of bend axis.
Use “loose leaf” constructions for multilayer flex in rigid flex.
No PTH’s in bend area.
Rout traces 90° to bend axis in bend area.
Avoid “I-Beam” routing of traces.
Use “cross hatch” reference places when possible.

## Slide 38: “Loose Leaf” Rigid Flex
No bonding between coverlays

## Slide 39: Bend Area for Rigid Flex
Bend Area

## Slide 40: Use of Stress Riser and Fillets
Risk of crack

## Slide 41: Ecobond Fillets for transition stress relief

## Slide 42: Tear Stops and No Square Corners or Sharp Edges

## Slide 43: Plating: Holes and Pads= OK, but don’t Plate Traces
Electroless
Nickel SEM
Rolled Annealed Copper

## Slide 44
Avoid “I-Beam” Circuit Lay-out
Not This This

## Slide 45
Can closely estimate impedance from stackup
  Take note of required values
    Dielectric Thickness, Copper Thickness, Copper Widths, Coverlay Thickness
    Dielectric Constant of Clad, Dielectric Constant of Coverlay, Spacing Between Lines
Cross Hatched Ground Planes
  Significantly increases impedance
  Shielding may poorer as a result
  If ground plane is gridded, then find out
    Width of Hatches (HW)
    Pitch of Hatches (HP)
    Angle (default is 45 degrees)

## Slide 46: Crosshatched Reference Planes Good for assembly *Moisture egress Good for Flexibility Has signal performance limitations

## Slide 47: Reference Plane design (12” x 18”)

## Slide 48: Stripline – Passband/Stopband

## Slide 49: Pyralux APR
Embedded Resistors
  Film under copper foil
  Selectively etched to form resistors
Series resistors

## Slide 50: Wrap-Up
Flex is growing;
Medical, Aero and outer space, Automotive, etc.
Speeds and low loss needs are increasing.
Many applications for electronics are possible;
Work with the fabricator early
New materials
AG, GPL, HT, etc

## Slide 51: Special thanks to:
Royal Flex Circuits Team
DuPont Electronic Solutions
Dale Smith

## Slide 52: Questions?
Email Lisa@royalcircuits.com, riki@royalflexcircuits.com or CHunrath@Insulectro.com with additional questions

## Slide 53: Thank you!
– Royal Flex Circuits
Chris Hunrath – Insulectro